## Slide 1
West Pro Series

## Slide 2
Product line
PRO-8
Industrial Controller
Standard Controller for
Process industry
PRO-4
PRO-16
Compact Industrial Controller

## Slide 3
PRO-8 Universal Industrial Controller

## Slide 4: Pro-8 Universal Controller

## Slide 5: PRO-8 Features
Alarm functions with optional latch
Maintenance manager and error list
Automatic/manual key
BluePort interface
Start-up circuit and boost function
Alarms for heating current & control loop
Optimization at set-point
Configurable function key

## Slide 6: PRO-8 Additional Features
Extended operating temperature up to 60 °C
  mounting close to the process
Universal version: continuous/switching output
  reduced stocks of spare parts
100 ms cycle time
  suitable for fast control loops
Special linearization for RTD‘s
  KTY, PTC, NTC, Pt 1000, Ni 100, Ni 1000, ...
Freely configurable analog output
  11-bit resolution
  galvanic isolation

## Slide 7
PRO-8 Additional Features
RS 422/485 MODBUS RTU interface
  MODBUS master configurable
  connection to SCADA software, OPC servers, PLC’s, etc
Built-in transmitter supply
  galvanic isolation
  direct and economic connection of 2 and 3-wire transmitters
Two parameter sets for gain scheduling
3-point controller for water, fan and oil cooling
Profiler with 10 Segments and events
Maintenance manager and error list

## Slide 8: Applications
Extruders
Hot Runners
Furnaces and Ovens
Burners and Boilers
Plastic Processing
Packaging
Driers
Climatic Chambers
Heat Treatment Plants

## Slide 9
PRO-4 Industrial and Process Controller

## Slide 10: PRO-4 Industrial Process Controller

## Slide 11: PRO-4 Features
Alarms for heating current & control
loop & actuator
Maintenance manager and error list
Day & Night display shows bar graphs
and plain text
BluePort interface
Two universal inputs
Limit signaling function with latch
Optimization at set-point
Configurable function key

## Slide 12: Control Features
Signaler (= ON/OFF control)
2-point controller
  relay or
  logic
continuous controller
  0/4...20mA or
  0/2...10V
3-point
  relay / relay
  relay / logic
  logic / logic
  continuous / continuous
  continuous / relay
  continuous / logic
motorized valve controller
  with position feedback
  with positioner
special algorithm for water, oil and fan cooling

## Slide 13: Highlights
Universal version: continuous/switching output
  Reduced stock of spare parts
100 ms cycle time
  suitable for fast control loops
Special linearization for all sensors
  thermocouples, RTD's, mA, V, mV
2 freely configurable analog outputs
  11-bit resolution
  galvanic isolation from the inputs.
Extended operating temperature up to 60 °C
RS 422/485 Modbus RTU interface
Profibus-DP
Built-in transmitter supply
  Galvanic isolation
  Direct and economic connection of 2 & 3 wire transmitters
Two parameter sets for gain scheduling
Programmer version available

## Slide 14: Highlights
INP2
Process value input
INP3
thermocouple or 0...100mV
Pt100, Pt1000, RTD or potentiometer
0(4)...20 mA or 0...10 Volt
e.g. heating current, setpoint, position feedback,...
0(4)...20 mA
0...50 mA AC for heating current 50A/1000
potentiometer up to 4500 Ohm
thermocouple or 0...100mV
Pt100, Pt1000, RTD or potentiometer
0(4)...20 mA.
INP1
e.g. 2nd process value, limit monitoring, display, ..

## Slide 15
PRO-16 Universal Process Controller

## Slide 16
PRO-16 Compact Industrial Process Controller

## Slide 17
Panel Mounted 48 x 48mm Temperature Controller by WEST
A compact, fully-featured controller for your
demanding applications
With 16 Profiles with up to 16 Segments
The only controller of its size, flexible with up to 6 outputs, 2 digital inputs, a remote setpoint input, RS485 communications and linked to best in class BlueControl software.
PRO-16

## Slide 18: Highlights
Flexible Options (built to order)
BlueControl© Software
Up to 6 outputs (relay, logic SSR, Linear DC)
Up to 4 digital Inputs
Heater current input
Transmitter power supply
RS485 communications
16 segments x 16 profiles
Parameter configuration
Save ‘recipes’ for production changes.
Clone other devices – ideal for OEMs
Simulator to test operation before going live.
Profile configuration with graphical overview.

## Slide 19: Applications
Oven and Furnaces
Chiller and Refrigeration Systems
Laboratory and Test Equipment
Boiler and Steam Processes
And a wide range of others

## Slide 20: Inputs
Thermocouple L, J, K, N, S, R, T, B, C, D, E
Input impedance ≥1MΩ
Cold junction compensation max additional error ±0.5K
Sensor break detection ≤1μA, configurable output action
RTD 3 Wire PT100, PT1000, KTY11-6,
Lead resistance max 30Ω
Input circuit monitor break and short circuit
DC Linear 0 to 10V, 0 to 20mA
Scaling selectable -1000…9999
Accuracy ≤2K Thermocouple (B type ≤3K), ≤1K PT100, ≤2K PT1000, 0.1% Linear DC
Temperature Effect <100ppm/K
Resolution to 3 decimal places
Sampling 10 per second, 100mS
Scaling single point offset or 2-point
"Digital Inputs (base unit)" Potential free ‘dry’, contact 3.3V, <10mA.
"Digital Inputs (optional)" 24V external excitation, reinforced isolation from other inputs and outputs
Heater Current Input Ranges 0 to 30mA ac , Scaling adjustable -1999 to 9999
Remote setpoint Range 0 to 20mA dc, Scaling adjustable -1999 to 9999

## Slide 21: Outputs
Single relay
  "Potential-free changeover contact, Max. contact rating: 2A at 250 V, 48...62
  Hz, resistive load, Operating life 150,000 duty cycles with max. rating.
  Operating life 250,000 duty cycles with 1A at 250 V, 48...62 Hz, resistive load,
  Minimum contact rating 6V, 1mA"
Dual Relay
  "2 NO contacts with common, Connection, Max. contact rating: 2A at 250 V,
  48...62 Hz, resistive load, Operating life 200,000 duty cycles with max. rating.
  Operating life 500,000 duty cycles with 1A at 250 V, 48...62 Hz, resistive load,
  Minimum contact rating 6V, 1mA"
Isolation Reinforced isolation from other inputs and outputs
Single SSR SSR driver voltage >10V into 500Ω minimum.
Dual SSR SSR driver voltage >10V into 500Ω minimum.
Linear DC 0-20mA, 4-20mA, 0-10V, 2-10V, 0.25% accuracy
Resolution Eight bits in 250mS (10 bits in 1s typical, >10bits in >1s typical)
Load impedance 0-20mA, 4-20mA 500Ω maximum, 0-10V 500Ω minimum
Isolation Reinforced isolation from other inputs and outputs
Transmitter Power Supply 22 mA / ≥18 V

## Slide 22: Technical Specification
Serial communications Physical: RS485, at 1200, 2400, 4800, 9600 or 19200 bps. Modbus RTU protocol
Environmental
Protection IP65 fascia, IP20 rear with terminal block mated.
Temperature and RH "For specified accuracy: Operation 0...60°C Storage: -20...70°C. Humidity 20 to 95% non condensing "
Altitude <2000m
EMC Complies with EN 61 326-1
General
Power Supply AC supply, Voltage: 90...260 V AC, Low voltage 20 to 48VAC 50/60Hz or 22 to 65VDC, 11.5VA
Housing ABS AF 305, flammability class UL 94 VO self extinguishing
Safety Complies with EN 61010-1 (VDE 0411-1):, Overvoltage category II, Contamination class 2, Working voltage range 300 V, Protection class II
Connections 5mm COMBICON connectors
Weight 0.2Kg
Mounting Panel mounting with quick release mounting clamp (supplied)
Standards CE, UL, cUL (options highlighted in green, pending other configurations)

## Slide 23: Product Part Code (Provisional)

## Slide 24
BlueControl©

## Slide 25
BlueControl - Software
Configuration, simulation and trend recording
Fast configuration
Reliable copying
Comprehensive off-line test
Data storage and documentation
Quicker commissioning
Do all of this on your PC, without opening the control cabinet, because ...
Pro-4 & -8 controllers have the BluePort!
Pro-16 controller done thru Comm port!

## Slide 26
BlueControl in 3 Versions
Mini version
  controller configuration (download)
  the simulation is an integral part!
  up- / down- loading, online and trend with simulation
Basic version
  up and down-loading
  online communication
  trend display
Expert version
  configurable trend display (in preparation)
  extended simulation
  program editor
  diagnostics
Free download from
www.west-cs.com

## Slide 27
Parameter and Configuration
Logical structure with parameter and configuration.
Submenu, like in the controller
Configuration-Code and plain text display
Mode-selection
Fade out inactive parameters

## Slide 28
Visibility
Mode-selection
Fade out whole menus in the equipment
Fade out individual parameter in the equipment

## Slide 29
Extended operation level and Display 2/3
Mode- selection
Selection parameter and signal
Copy into the extended operation level
Copy into the Display 3
Copy into the Display 2

## Slide 30
Communication BlueControl - Controller
Permanent connection for e.g. start-up and trend recording
Read all parameters of the controller
Write all parameters of the controller

## Slide 31
Online mode of operation

## Slide 32
Online mode of operation
Display and modify process values
Trend
Diagnostic

## Slide 33
Online mode of operation....
Display of process values
Modify of the setpoint
Switching e.g. to manual
Start of the self tuning
Display the process
Alarm status
Reset the error list

## Slide 34
Online mode of operation....
Recording of analog-signal
Recording of digital-signal

## Slide 35
Online mode of operation....
Current parameter value list by color
Recording interval of 100ms up to 20 seconds
Record up to 40 hours
Two scales at same time (e.g. controller output and process value)
Measuring cursor to accurately determining of individual values
Exporting of data to CSV format for use by other programs e.g. Excel
Zoom of arbitrary ranges

## Slide 36
Online mode of operation....
Device information
  Order number
  SW-version
  Identification number
Device diagnostic
  Max. measured temperature
  Result of the self test
Device monitoring
  Operating hours
  Output switching
Error list
  Complete error list
  Reset

## Slide 37
The Simulation
Display like the controller
Operation
Select input-values
Simulation of the process
or
Indication of the outputs
Turbo
Pause
Process parameters
On / Off

## Slide 38
The Simulation - Setting of the process
Store different process
Setting of the process parameters
For cooling separately
Store different disturbances

## Slide 39
Program Editor (Expert)
Copy to or from other programs, I.e. Excel
Program Selection
Segments can be copy and pasted.
Ability to ‘draw’ the profile
Time proportional representation

## Slide 40
Program Editor (Expert)
or
Segment number
Segment type
Setpoint
Ramp Time
Ramp Rate
Event Status

## Slide 41
Thank You
www.West-CS.com/LP/Pro-Series